## Slide 1: Joint Capacity Planning and Operational Management for Sustainable Data Centers and Demand Response
Tan N. Le, Zhenhua Liu, Yuan Chen, and Cullen Bash
June 21, 2016
Notes: Introduce my self
I am a Phd Student from Stony Brook University, NY.
This joint work with my advisor Dr. Zhenhua Liu, and 2 co-authors from HP labs Yuan Chen and Cullen Bash

## Slide 2: Agenda
Introduction & Motivation
Proposed Optimization Framework
Numerical Evaluation
Data Center Demand Response
Conclusions & Future Directions

## Slide 3
Total Global Cloud Traffic Growth
www.cisco.com
Notes: The total data center traffic has been significantly increasing at 25% at year as the high demand from the Internet users.
Especially, could data centers are significantly increasing
Source: http://www.cisco.com/

## Slide 4: Environmental threat from data centers
Carbon footprints of servers can vary by 10x, www.vertatique.com
E. Facts. Greenhouse gas emissions from a typical passenger vehicle, 2005.
=
450W
5.2 tons carbon a year
Chart: 
| Argentina | Czech Republic | US Data centers | Romania | Denmark
megatons carbon | 199 | 112 | 100 | 78 | 59
www.nrdc.org & wikipedia.org
Emissions in 2013
Notes: High light the emission

## Slide 5
How much do data centers cost?
http://www.datacenterknowledge.com/
Where do the costs come from?
Notes: How much do data centers cost?

## Slide 6
Capacity Planning
(CP)
Operational
Management
(OM)
Traditionally, they are separate
servers
Power sources
cooling
electricity bills
maintenance
fuel
What are the drawbacks of separate CP & OM?
Notes: Emphasize that Capacity Planning and Operational Management are separate
Highlight that staff salary is small
What is the drawback?

## Slide 7: CP based on the peak demand
Power demand of a data center
Over capacity planning
Demand
Supply
good news
Power demand can be shaped
Traditional Capacity Planning
Notes: This is a example of how people do capacity planning.
Todo: Cite

## Slide 8: Shaping power demand
Scheduling the batch jobs
[Aksanli SIGOPT’12 ]
Optimize cooling power
[Pakbaznia ISLPED’09,
Liu SIGMETRICS’12]
Geographical load balancing
[Qureshi SIGCOMM’09, Liu SIGMETRICS’ 11]
Network consolidation
[Zhang ICNC’10, Andrews ToN’12]
Server consolidation [Lin ToN’13, Zhang ICAC’12]
~500kW
~400kW
Waste of 20% of supply & demand
There so many data center demand management techniques
Notes: Shifting the batch job workload
500

## Slide 9: Agenda
Introduction & Motivation
Proposed Optimization Framework
Numerical Evaluation
Data Center Demand Response
Conclusions & Future Directions

## Slide 10
Joint
Proposed Optimization Framework
Capacity Planning
(CP)
Operational
Management
(OM)
Notes: Proposed Framework

## Slide 11: Modelling power demand at time year
where
starting time  ending time
interactive workloads
: power for workload
batch jobs
: power for job
total IT power
idle power
total power

## Slide 12: Modelling power supply at time year
renewable generators : capacity of generator
Generation where CF is capacity factor.
non-renewable generators : Capacity of generator
generation
Electricity grid
grid power
sell-back power

## Slide 13: Joint Optimization Framework
minimize UtilBill + RGEx + NGEx + ITEx
Utility bills (UtilBill)
RG Expense (RGEx)
NG Expense (NGEx)
IT expense (ITEx)
Infrastructure cost
+ O&M cost
Infrastructure cost
+ Fuel cost
+ O&M cost
Infrastructure cost
+ O&M cost
Purchase
– sellback
Notes: Utility bills

## Slide 14
Inputs (forecasted)
Workload traces
Electricity prices
Infrastructure cost
O&M cost
Emission rate
Capacity planning outputs
Capacities of renewables
Capacities of non-renewables
Capacity of IT power demand
Capacity of Electricity grid
Operational management outputs
non-renewable generation
Grid power usage
Sell-back power
Power allocated to IT workloads
Joint
Optimization
Framework
Notes: Optimization problem

## Slide 15: Agenda
Introduction & Motivation
Proposed Optimization Framework
Numerical Evaluation
Data Center Demand Response
Conclusions & Future Directions

## Slide 16
www.hp.com HP EcoPODs 240a
7 year simulation based on 1MW HP EcoPod Data Center

## Slide 17: Demand side
Peak power usage: 720kW
Peak-to-Mean ratio: 3
PUE: 1.2
CPU power usage trace
Interactive workload: 50%
Utilization of server: 40%
Batch jobs: 50%
~ 24 hours
Maximum utilization is 90%
Notes: Todo: cite the trace? From SAP?

## Slide 18
Supply side
Houston PV generation
Max capacity: 1MW
Amortized cost: $2.15/W a year
Operational cost: $0/kWh
Maintenance cost: $0.005/kWh
Capacity factor: Houston trace
PV generation
General Electric (GE)
Natural Gas generation
Amortized cost: $1/W a year
Operational cost: $0.06/kWh
Maintenance cost: $0.005/kWh
Efficiency: 30%
Electricity grid
Prices: $0.056/kWh

## Slide 19: Comparisons with Baseline methods
Grid Only (GRID) in traditional data centers Only provision power from the electricity grid
Demand-only Optimization (DEM) Optimize power demand based on given the capacity planning
Supply-only Optimization (SUP) Optimize power sources based on given demand
Proposed framework (PROP) = SUP + DEM

## Slide 20
How much cost savings and emission reductions?
GRID: Grid only
DEM: Demand-only optimization
SUP: Supply-only optimization
PROP: Proposed framework
I: Infrastructure
O: Operational
Util: Utility bill
Cost: PROP = 50 % GRID
Emissions: PROP = 25 % GRID
Notes: Grid: Grid only
Dem: Demand-only optimization
Sup: Supply-only optimization
Prop: Proposed framework

## Slide 21: Costs and Emissions under Prediction Errors
58%
49%
Expenditures vs. prediction errors
Emissions vs. prediction errors
PROP significantly outperforms GRID under large prediction errors
Notes: PROP significantly outperforms GRID under large prediction errors
58%

## Slide 22: Agenda
Introduction & Motivation
Proposed Optimization Framework
Numerical Evaluation
Data Center Demand Response
Conclusions & Future Directions

## Slide 23: How demand response (DR) works
DR signal
Accept  reward
Reject  penalty
Grid condition
Notes: How demand response (DR) works by example

## Slide 24: Demand response programs
Active participations
Passive participations
DR signals are given to encourage customers to adjust their power profiles by using electricity prices
Time of Use (ToU): prices vary in different periods a day,
Inclining Block Rates (IBR): prices are based on load levels
Critical Coincident Peak Pricing (CPP): Very high prices for coincident peaks
Ancillary services to maintain the reliability of grid, e.g., Spinning Reserve (SR)
Wholesale markets (WS) offer cheap prices if purchasing ahead
Customers voluntarily to have DR contracts with Utilities
[Wierman ISGC’14]

## Slide 25
$0.05 (night), $0.219 (peak), $0.06 (off) /kWh
CPP rate: $11.2/kWh
$0.2 (<50kW), $0.5 (<100kW)
Without DR programs
Time of Use (ToU)
Critical Peak Pricing (CPP)
IBR
Base price: $0.056/kWh
SR rate: $0.02/kWh
Spinning Reserve (SR)
$0.05/kWh
Wholesale (WS) market
Notes: Without DR programs

## Slide 26: How DR impacts on data centers?
Little change on total costs
Some DR programs result in low emissions
Notes: Little change on total costs

## Slide 27: Agenda
Introduction & Motivation
Proposed Optimization Framework
Numerical Evaluation
Data Center Demand Response
Conclusions & Future Directions

## Slide 28: Conclusions
This work is motivated by the huge expenses on capacity planning and operational management of data center
Proposed Joint Optimization framework for capacity planning and operational management
  50% cost savings
  75% emission reductions
Proposed framework
  promotes the use of renewable energy
  adapts well to DR programs

## Slide 29: Future Directions
Stochastic characteristics of workload and renewable energy in capacity planning and operational management
Capacity planning for geographically distributed data centers

## Slide 30
www.theodysseyonline.com

## Slide 32: Backup slides

## Slide 36
Impacts on
Net-zero energy data centers
Notes: Total local supply >= total demand in long-run

## Slide 37
Notes: the data center starts to use more GE to provide power during night and given the increased GE capacity, more GE generation is used during day time to replace PV.

## Slide 38
Notes: Especially, there is the sharp increase of PV capacity when the gas price is more than $0.06$.
Due to the non-dispatchability of solar energy, the data center needs the large capacity of PV generation to compensate the reduction of GE generation.