## Slide 1: Joint Capacity Planning and Operational Management for Sustainable Data Centers and Demand Response
Tan N. Le and Zhenhua Liu
June 22, 2016
Session 2: Energy-efficient Datacenters
tan.le@stonybrook.edu
Yuan Chen and Cullen Bash
Notes: Introduce my self
I am Tan Le, a Phd Student from Stony Brook University, NY.
This joint work with my advisor Dr. Zhenhua Liu, and 2 co-authors from HP labs Yuan Chen and Cullen Bash

## Slide 2
Total global cloud traffic growth
www.cisco.com
Notes: the global cloud traffic data keep growing at 35%
From 2012 -> 2017, the traffic can increase 4 times in 5 years
What are the consequences of this?

## Slide 3
http://www.datacenterknowledge.com/
Notes: The increase of cloud traffic need more data centers or larger data ceters.
Global cloud providers like Amazon, Microsoft, IBM, and Google
First, the growth of cloud service demand results in more investment in data centers

## Slide 4: Environmental threat from data centers
Carbon footprints of servers can vary by 10x, www.vertatique.com
E. Facts. Greenhouse gas emissions from a typical passenger vehicle, 2005.
=
450W
5.2 tons carbon a year
Chart: 
| Argentina | Czech Republic | US Data centers | Romania | Denmark
megatons carbon | 199 | 112 | 100 | 78 | 59
www.nrdc.org & wikipedia.org
Emissions in 2013
Notes: In addition, data centers are not CLEAN.
The emissions from a single server in a data center can be equivalent to a car.
Lets look at this graph, it shows the amount of emissions from US data centers are even more than some countries in Europe like Denmark and Romania.
And, it is growing~

## Slide 5: Goal: Reduce costs and emissions for data centers with renewables
Approach: Joint Optimization of CP and OM
Modeling
Evaluation
Capacity Planning (CP)
Operational
Management
(OM)

## Slide 6
Capacity Planning (CP)
Operational Management (OM)
Traditionally, they are separate
servers
Power sources
cooling
electricity bills
maintenance
fuel
This results in significant inefficiencies
Ex: CP is based on peak demand, but peak can be shaped in OM
Notes: Emphasize that Capacity Planning and Operational Management are separate
What is the drawback?

## Slide 7
Proposed Joint Optimization Framework
Capacity Planning (CP)
Operational
Management
(OM)
Capacities of renewables,
Non-renewables, IT power demand
Non-renewable generation
Batch job schedule
Grid power usage
Sellback power
Notes: Proposed Framework

## Slide 8: Joint Optimization Framework
minimize
Utility bills (UtilBill)
Renewable Generation Expense (RGEx)
Non-renewable Generation Expense (NGEx)
IT expense (ITEx)
UtilBill
+ RGEx
+ NGEx
+ ITEx
CP cost | N/A | Infra. Cost | Infra. Cost | Infra. cost
OM cost | Purchase – Sell back | O&M costs | O&M costs | O&M costs
The optimization problem is convex
Notes: Utility bills

## Slide 9: How the framework operates?
Inputs (forecasted)
Workload traces
Electricity prices
Infrastructure costs
O&M costs
Capacities
Renewable generation
non-renewable generation
IT power demand
Operational outputs
non-renewable generation
Grid power usage
Sell-back power
Power allocated to batch jobs
Capacity Planning (CP)
Operational
Management
(OM)
Joint Optimization Framework
Solve optimization problem
Notes: DONE with modeling!!

## Slide 10: Goal: Reduce costs and emissions for data centers with renewables
Approach: Joint Optimization of CP & OM
Modeling
Evaluation
Capacity Planning (CP)
Operational
Management
(OM)
Notes: Lets see how the proposed framework benefit the data centers!!!

## Slide 11
HP EcoPODs 240a
Simulation based on 1MW HP EcoPod Data Center
www.hp.com

## Slide 12: Demand Side
Peak-to-Mean ratio: 3
PUE: 1.2
Annual increase rate: 9% a year
CPU power usage trace
Interactive workload: 50%
Utilization of server: 40%
Batch jobs: 50%
Flexibility 24 hours
Maximum utilization is 90%
We do not include capacity planning for IT equipment
[www.zdnet.com]
Notes: We do not include capacity planning for IT equipment

## Slide 13
Infra. cost: $2.15/W a year > Infra. cost: $1/W a year > Infra. cost: $0/W a year
Supply Side
[Houston traces]
PV generation
General Electric (GE)
Natural Gas generation
Electricity grid
Operational cost: $0/kWh < Operational cost: $0.06/kWh > Price: $0.056/kWh
Maintenance cost: $0.005/kWh = Maintenance cost: $0.005/kWh > Maintenance cost: $0/kWh
Emission rate: 0.034g/kWh < Emission rate: 0.443g/kWh > Emission rate: 0.5g/kWh
Capacity factor: ~18%
12% a year
1% a year
5% a year
[Texas]
[Texas]
[www.eia.com]
[cleantechnica]
Notes: Todo: add the trend for PV, GE, and Electricity prices
12%

## Slide 14: Comparisons with baseline methods
Grid Only (GRID) in traditional data centers provisions power only from the electricity grid
Demand-only Optimization (DEM) optimizes power demand based on given the capacity planning
Supply-only Optimization (SUP) optimizes power sources based on given demand
Proposed framework (PROP) Joint Capacity Planning & Operational Management
Notes: Explain GRID
Explain SUP
Explain

## Slide 15
Question: How much can we improve?
GRID: Grid only
DEM: Demand-only optimization
SUP: Supply-only optimization
PROP: Proposed framework
I: Infrastructure
O: Operational
Util: Utility bill
Cost: PROP = 50 % GRID
Emissions: PROP = 25 % GRID
Notes: Explain the bread down cost:
For Grid-only method, cost comes from the utility bills.
SUP has more PV-I

## Slide 16: Costs and emissions under prediction errors
Expenditures vs. prediction errors
Emissions vs. prediction errors
PROP significantly outperforms GRID under large prediction errors
49%
58%
Notes: Mean value = 1, RMSE is 0->0.7
Prediction errors are applied to all predicted value.
Predictions are independent among the sources
Explain the normalized errors: RMSE errors = 50% of mean value

## Slide 17
Cost saving 50%
Emission reduction 75%
Joint Capacity Planning and Operational Management
Notes: Here we know that our proposed can significantly benefit the data centers

## Slide 18: Goal: Reduce data center costs with Demand Response
Approach: Joint Optimization of CP & OM
Modeling
Evaluation
Capacity Planning (CP)
Operational
Management
(OM)

## Slide 19: Extending Joint Optimization Framework for DCDR
minimize
Utility bills (UtilBill)
Renewable Generation Expense (RGEx)
Non-renewable Generation Expense (NGEx)
IT expense (ITEx)
UtilBill
+ RGEx
+ NGEx
+ ITEx
CP cost | N/A | Infra. cost | Infra. Cost | Infra. cost
OM cost | Purchase – Sell back | O&M costs | O&M costs | O&M costs
- DR reward + DR penalty
Notes: Utility bills

## Slide 20: Operation of Framework in DR programs
$0.05 (night), $0.219 (peak), $0.06 (off) /kWh
Without DR programs
Time of Use (ToU)
Base price: $0.056/kWh
SR rate: $0.02/kWh
Spinning Reserve (SR)
SR hour
Data center additionally provisions PV & GE to adapt to DR programs
night
peak
off-peak
peak is shifted
Load reduction
Notes: Without DR programs

## Slide 21: Question: How DR impacts on data centers?
Costs & capacities vary in different DR programs
Some DR programs result in low emissions
IBR: Inclining Block Rates
WS: Wholesale market
CPP: Critical Coincident Peak Pricing
CPP rate: $11.2/kWh
$0.2 (>50kW), $0.5 (>100kW)
$0.05/kWh
PV & GE are used
Low emissions due to PV
Notes: IBR: Inclining Block Rates

## Slide 22
Cost saving 50%
Emission reduction 75%
Joint Capacity Planning and Operational Management
Well adapting to
Thank you
Notes: This is the end of presentation.
Traditionally, capacity planning and operational management are separate
We proposed ….
It can achieve up to 50% cost
75 % emission reduction
Make the the data center well adapt to the DR programs
Thank you

## Slide 24: Backup slides

## Slide 28: Modeling power demand at time year
: power for job
interactive workloads
batch jobs
IT power:
idle power
power demand:
: power for workload
starting time  ending time
used to schedule batch jobs

## Slide 29: Modeling power supply at time year
renewable generators
where CF is capacity factor.
: capacity of generator
non-renewable generators
: Capacity of generator
Electricity grid
grid power
sell-back power
power supply:
power supply power demand

## Slide 30
Impacts on
Net-zero energy data centers
Notes: Total local supply >= total demand in long-run

## Slide 31
Notes: the data center starts to use more GE to provide power during night and given the increased GE capacity, more GE generation is used during day time to replace PV.

## Slide 32
Notes: Especially, there is the sharp increase of PV capacity when the gas price is more than $0.06$.
Due to the non-dispatchability of solar energy, the data center needs the large capacity of PV generation to compensate the reduction of GE generation.

## Slide 34
$0.05 (night), $0.219 (peak), $0.06 (off) /kWh
CPP rate: $11.2/kWh
$0.2 (<50kW), $0.5 (<100kW)
Without DR programs
Time of Use (ToU)
Critical Peak Pricing (CPP)
IBR
Base price: $0.056/kWh
SR rate: $0.02/kWh
Spinning Reserve (SR)
$0.05/kWh
Wholesale (WS) market
Notes: Without DR programs